## Slide 1: Ankara University Computer Engineering Department COM325 Microprocessors Lab 2
Metehan Ünal

## Slide 2: Q-1
What do the following MOV instructions accomplish?
  MOV AX, BX
  MOV CH,3AH
  MOV [4815H],AX
  MOV [BX] , CL
  MOV ES,DS
  MOV BL,DX
  MOV CS,AX

## Slide 3: A-1
What do the following MOV instructions accomplish?
  MOV AX, BX  Copies BX into AX (Register)
  MOV CH,3AH  Copies Data 3AH into CH (Immediate)
  MOV [4815H],AX  DSx10H + DISP = 10000H + 4815H Copies AX into 14815H (Direct)
  MOV [BX] , CL DSx10H+BX = 10000 + 0500H  Copies CL into 10500H (Register Indirect)
  MOV ES,DS  Segment to Segment is not allowed!
  MOV BL,DX  Mixed Size is not allowed!
  MOV CS,AX  Code Segment can not be destination!

## Slide 4: Q-2
List the 8-bit and 16-bit registers that are used for register addressing.

## Slide 5: A-2
List the 8-bit and 16-bit registers that are used for register addressing.
  8-bit Registers: AH, AL, BH, BL, CH, CL, DH, DL.
  AX, BX, CX, DX, SP (Stack Pointer), BP (Base Pointer), SI, DI.

## Slide 6: Q-3
Select an instruction for each of the following tasks:
  copy 12H into AL
  copy CX into AX
  copy 100 into BL
  copy the Word contents of the data segment memory location addressed by BX into AX
  copy the AX register into stack.
  remove a word from the stack and place it into the DX
  copy AX, CX, DX, BX, SP, BP, DI and SI to the stack using minimum instruction.

## Slide 7: A-3
Select an instruction for each of the following tasks:
  copy 12H into AL  MOV AL,12H
  copy CX into AX MOV AX,CX
  copy 100 into BL  MOV BL, 100 MOV BL, 64H
  copy the Word contents of the data segment memory location addressed by BX into CX  MOV CX, [BX]
  copy the AX register into stack PUSH AX
  remove a word from the stack and place it into the DX  POP DX
  copy AX, CX, DX, BX, SP, BP, DI and SI to the stack using minimum instruction. PUSHA

## Slide 8: Q-4
Suppose that DS = 0200H, AX = 2400H, BX = 0300H, DI = 400H, ARRAY = 5100H, and DX=1234H. Determine the memory address accessed by each of the following instructions, assuming real mode operation :
  MOV AL,[1234H]
  MOV EAX,[BX]
  MOV [DI],AL
  MOV AX, [DI+100H]
  MOV ARRAY[BX], DX

## Slide 9: A-4
Suppose that DS = 0200H, AX = 2400H, BX = 0300H, DI = 400H, ARRAY = 5100H, and DX=1234H. Determine the memory address accessed by each of the following instructions, assuming real mode operation :
  MOV AL,[1234H]  DSx10H + 1234H =2000H+1234H =3234H
  MOV EAX,[BX]  DSx10H+BX = 2000H+300H = 2300H
  MOV [DI],AL  DSx10H+DI = 2000H + 400H=2400H
  MOV AX, [DI+100H]  DSx10H + DI +100H = 2000H + 400H +100H =2500H
  MOV ARRAY[BX], DX  DSx10H + ARRAY + BX = 2000H + 5100H = 0300H = 7400H

## Slide 10: Q-5
Assume that CS = 1900H and IP=1740H; find the address of the next instruction to be executed.

## Slide 11: A-5
Assume that CS = 1900 and IP=1740; find the address of the next instruction to be executed.
  CSx10H +IP  19000H + 1740H =1A740H

## Slide 12: Q-6
What is wrong with a MOV [BX],[DI] instruction?

## Slide 13: A-6
What is wrong with a MOV [BX],[DI] instruction?
  Memory-to memory moves are not allowed.

## Slide 14: Q-7
What are the program memory-addressing modes?

## Slide 15: A-7
What are the program memory-addressing modes?
  Direct,
  Relative,
  Indriect.

## Slide 16: Q-8
What segment register may not be popped from the stack?

## Slide 17: A-8
What segment register may not be popped from the stack?
  Code Segment (CS)

## Slide 18: Q-9
Explain what happens when the PUSH BX instruction executes. Make sure to show where BH and BL are stored. (Assume that SP = 0100H and SS = 0200H

## Slide 19: A-9
Explain what happens when the PUSH BX instruction executes. Make sure to show where BH and BL are stored. (Assume that SP = 0100H and SS = 0200H
  BH is stored in 20FF
  BL is stored in 20FE
  The stored value in SP decreased by two and becomes 00FE.

## Slide 20: Q-10
The 16-bit POP instruction (except for POPA) increments SP by ____________.

## Slide 21: A-10
The 16-bit POP instruction (except for POPA) increments SP by ______2______.

## Slide 22: Q-11
Explain what happens when following instructions are executed.
  LEA BX, [DI]
  LDS BX, [DI]
  LODSB
  LODSW
  STOSB
  STOSW
  XCHG AL, CL

## Slide 23: A-11
I. LEA BX, [DI]
  LEA: Loads a 16 or32 bit register with the offset address of the data specified by the operand.
  LEA BX, [DI]; loads the offset address specified by [DI], contents of DI into BX register.
  MOV BX, [DI]; loads the data stored at the memory location addressed by [DI] into register BX
  MOV BX, OFFSET DATA1; same as LEA BX, DATA1

## Slide 24: A-11
II. LDS BX, [DI]
  LDS: Loads any 16 or32 bit register with an offset address and the DS segment register with a segment address.
  LDS BX, [DI]; Transfers the 32 bit number addressed by DI in the data segmentin to BX and DS registers

## Slide 25: A-11
LODS: Loads AL or AX with data stored at the data segment offset address indexed by the SI register
III. LODSB
  LODSB -> AL = DS:[SI]
  SI = SI ±1
IV. LODSW
  LODSW-> AX = DS:[SI]
  SI = SI ±2

## Slide 26: A-11
STOS: Stores AL or AX at the extra segment memory location addressed by the DI register LEA BX, [DI]
V. STOSB
  STOSB ->ES:[DI] = AL
  DI = DI ±1
VI. STOSW
  STOSW-> ES:[DI] = AX
  DI = DI ±2

## Slide 27: A-11
VII. XCHG AL, CL
  Exchanges the contents of a register with the contents of any other register or memory location.
  XCHG AL, CL => Exchanges the contents of AL and CL.