## Slide 1: SPATIAL FILTERING

## Slide 2: NEIGHBOURHOOD OPERATIONS
simply operate on a larger neighbourhood of pixels than point operations
Neighbourhoods  mostly a rectangle around a central pixel
Any size rectangle and any shape filter are possible
Origin
x
y
Image f (x, y)
(x, y)
Neighbourhood

## Slide 3: NEIGHBOURHOOD OPERATIONS
Some simple neighbourhood operations :
  Min: Set the pixel value to the minimum in the neighbourhood
  Max: Set the pixel value to the maximum in the neighbourhood
  Median: The median value of a set of numbers is the midpoint value in that set (e.g. from the set [1, 7, 15, 18, 24] 15 is the median). Sometimes the median works better than the average

## Slide 4: THE SPATIAL FILTERING PROCESS
r
s
t
u
v
w
x
y
z
Origin
x
y
Image f (x, y)
eprocessed = v*e + r*a + s*b + t*c + u*d + w*f + x*g + y*h + z*i
Filter
a
b
c
d
e
f
g
h
i
Original Image Pixels
repeat for every pixel in the original image to generate the filtered image

## Slide 5: THE SPATIAL FILTERING

## Slide 6: THE SPATIAL FILTERING - SMOOTHING
One of the simplest spatial filtering operations we can perform is a smoothing operation
  Simply average all of the pixels in a neighbourhood around a central value
  Especially useful in removing noise from images
  Also useful for highlighting details
Simple averaging filter

## Slide 7: THE SPATIAL FILTERING - SMOOTHING
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
Image f (x, y)
e = 1/9*106 + 1/9*104 + 1/9*100 + 1/9*108 + 1/9*99 + 1/9*98 + 1/9*95 + 1/9*90 + 1/9*85
= 98.3333
Filter
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
1/9
104
100
108
99
106
98
95
90
85
Original Image Pixels
*
Origin

## Slide 8: Smoothing Example
The image at the top left is an original image of size 500*500 pixels
The subsequent images show the image after filtering with an averaging filter of increasing sizes
  3, 5, 9, 15 and 35
Notice how detail begins to disappear

## Slide 9: Weighted Smoothing Filters
More effective smoothing filters by allowing different pixels in the neighbourhood different weights in the averaging function
  Pixels closer to the central pixel are more important
  Often referred to as a weighted averaging
Weighted averaging filter
Distance =1 px
Distance =1.4 px

## Slide 10: Weighted Smoothing Filters
More effective smoothing filters by allowing different pixels in the neighbourhood different weights in the averaging function
  Pixels closer to the central pixel are more important
  Often referred to as a weighted averaging
Weighted averaging filter
Distance =1 px
Distance =1.4 px

## Slide 11: Weighted Smoothing Filters
Filtering is often used to remove noise from images
Sometimes a median filter works better than an averaging filter
Original Image With Noise
Image After Averaging Filter
Image After Median Filter
Still noisy

## Slide 12: Filtering At The EDGES
At the edges of an image we are missing pixels to form a neighbourhood
Origin
x
y
Image f (x, y)
e
e
e
e
e
e
e
?

## Slide 13: Filtering At The EDGES
  Pad the image
    Typically with either all white or all black pixels (ZERO PADDING)

## Slide 14: SPATIAL FILTERS - SHARPENING
Sharpening spatial filters  to highlight fine detail
  Remove blurring from images
  Highlight edges
Sharpening filters are based on spatial differentiation

## Slide 15: SPATIAL FILTERS - SHARPENING
Differentiation measures the rate of change of a function
It’s just the difference between subsequent values and measures the rate of change of the function
The formula for the 1st order derivative of a function is as follows:

## Slide 16: SPATIAL FILTERS - SHARPENING
The formula for the 2nd order derivative of a function is as follows:
Simply takes into account the values both before and after the current value

## Slide 17: SPATIAL FILTERS - SHARPENING
The 2nd order derivative is more useful for image enhancement than the 1st derivative
  Stronger response to fine detail
  Simpler implementation

## Slide 18: SPATIAL FILTERS – SHARPENING-LAPLACIAN
The Laplacian is defined as follows:
where the partial 2nd order derivative in the x direction is defined as follows:
and in the y direction as follows:

## Slide 19: SPATIAL FILTERS – SHARPENING-LAPLACIAN
So, the Laplacian can be given as follows:
We can easily build a filter based on this:
? | ? | ?
? | ? | ?
? | ? | ?

## Slide 20: SPATIAL FILTERS – SHARPENING-LAPLACIAN
So, the Laplacian can be given as follows:
We can easily build a filter based on this:
0
1
0
1
-4
1
0
1
0
f(x+1,y)
f(x+1,y-1)

## Slide 21: SPATIAL FILTERS – SHARPENING-LAPLACIAN
Applying the Laplacian  we get a new image that highlights edges and other discontinuities

## Slide 22: SPATIAL FILTERS – SHARPENING-LAPLACIAN
The result of a Laplacian filtering is not an enhanced image
Subtract the Laplacian result from the original image
  to obtain a sharpened enhanced image

## Slide 23: SPATIAL FILTERS – SHARPENING-LAPLACIAN
EDGES AND DETAILS ARE MUCH MORE OBVIOUS!

## Slide 24: SPATIAL FILTERS – SHARPENING-LAPLACIAN
EDGES AND DETAILS ARE MUCH MORE OBVIOUS!
ORIGINAL IMAGE (blurry)
SHARPENED IMAGE BY LAPLACIAN

## Slide 25: SPATIAL FILTERS – SHARPENING-LAPLACIAN
The entire enhancement  a single filtering operation

## Slide 26: SPATIAL FILTERS – SHARPENING-LAPLACIAN
The entire enhancement  a single filtering operation
0
-1
0
-1
5
-1
0
-1
0
A new filter that sharpens the image in one step

## Slide 27: 1st ORDER DERIVATE OPERATORS - SOBEL
-1
0
1
-2
0
2
-1
0
1
EDGE DETECTION!
They are sensitive to noise in the image, which can lead to false edge detection.
The positive values (+1 and +2) on the right side give more weight to pixels with higher intensity, emphasizing transitions from dark to bright as we move horizontally.
Similarly, the negative values (-1 and -2) on the left side emphasize transitions from bright to dark.
-1
-2
-1
0
0
0
1
2
1

## Slide 28: 1st ORDER DERIVATE OPERATORS - SOBEL
Gy for the pixel in row 2, column 2 is 315.
Gx for the pixel in row 2, column 2 is 315.

## Slide 29: 1st ORDER DERIVATE OPERATORS - SOBEL
magnitude(G) =
magnitude(G) =
magnitude(G) ≈ 445

## Slide 30: WHAT IF A PIXEL VALUE EXCEEDS 255?
445 | 0 | 255
200 | 0 | 0
210 | 155 | 255
=[(445-0)/(445-0)](255-0) + 0 = 255
255 | 0 | 146
115 | 0 | 0
120 | 89 | 146